## Slide 1: Nakuja Project
Avionics
Week 3 Progress Report

## Slide 2: Tasks completed this week
[#30] Research on camera
ESP32 CAM test
FPV Camera test
[#1] ESP Wi-Fi data transmission test
[#2] Research on ground station

## Slide 3: Research on camera
We found an ESP32 CAM module that communicates over WIFI Ip address
ESP32 cam uses OV2640 camera module-JPEG compressed image

## Slide 4: ESP32 CAM Specifications
The smallest 802.11b/g/n Wi-Fi BT SoC module
Low power 32-bit CPU, can also serve the application processor
Up to 160MHz clock speed, summary computing power up to 600 DMIPS
Built-in 520 KB SRAM, external 4MPSRAM
Supports UART/SPI/I2C/PWM/ADC/DAC
Support OV2640 and OV7670 cameras, built-in flash lamp
Support image Wi-Fi upload

## Slide 5: Test results
We conducted tests on video transmission over a range of 15m
Video results were received over IP address
Constrained by Wi-Fi Strength considering its operating over Wi-Fi
Good resolution up to distances of 5m. Beyond 15m, the camera lost its clarity

## Slide 6: FPV Camera test
Transmitter
Receiver

## Slide 7: Specs
Transmitter
Channels - 8
Frequency band - 2.4 – 6.8GHz
Receiver
Channels - 8
Frequency band - 2.4 – 6.8GHz

## Slide 8: Test results Test site: Sajorec, Distance ~1.1km
300m
100m

## Slide 9
500m
700m

## Slide 10
1km
Image started becoming grainy and pixelated at 1km

## Slide 11: Concerns
Interference with other Wi-Fi frequencies especially ESP32 Wi-Fi
Solution: Operate FPV on a different frequency
Directivity
At 300m we noticed that when the antennas are pointed towards each other the video signal is degraded compared to when they are held upright

## Slide 12: Concerns
Power usage
FPV transmitter uses 9-12 Volts. We intend to add a more powerful battery
Storage – Tweak the LCD-TFT receiver to include flight video storage

## Slide 13: [#2] Research on ground station 1. Flight Data Recorder
Aim: Receive data from esp32 to Raspberry Pi Serial monitor
We were able to fetch data received from ESP32 to Raspberry pi via the serial monitor and store in a csv file with python
Advantage: Graphing, Storage and analysis for future optimization

## Slide 14: Task this week
[#23] Avionics bay design
[#1] Wi-Fi Antenna design for range extension
[#2] Dashboard design
[#31] Apogee detection
[#26] Improve Kalman filter performance